Aroostook County, Maine

Amateur Radio Emergency Communications Frequency Plan

Call Channel		146.52 MHz	(Statewide Coordination)

## Repeaters

M1			146.73	MHz	-600 kHz	Presque Isle

M2			146.64 MHz	-600 kHz	Ft Kent tone 100 Hz

M3			145.17 Mhz	-600 kHz	Island Falls tone 123 Hz

link up, 171; link down, 170

M4			147.06 MHz	+600 kHz	(Perth-Andover, NB)

M5			147.39 MHz	+600 kHz	Fort Fairfield tone 123 Hz

## Simplex

M6			146.475 MHz		Aroostook County Primary

M7			147.510 MHz		Aroostook County Secondary

M8			147.525 MHz		Washington County Primary

M9			146.580 MHz		Penobscot County Primary

M10			154.055 MHz		AKEMA – receive-only

## HF - Statewide

Daytime		7.262 MHz LSB

Nighttime		3.940 MHz LSB

Revised 9/10/2013

NG1F